## Slide 1
📹
506
CAMERAS MONITORED DAILY
23
DVRs / NVRs
<5 min
Full Check Time
CCTV
SURVEILLANCE BOT
Automated Daily Camera Health Check System
for Aura Jewels Pvt. Ltd.
Hikvision ISAPI
Python + Flask
SQLite Database
Auto Excel Report
Aura Jewels Pvt. Ltd. | CCTV Operations | 2026

## Slide 2
📹
CCTV
SURVEILLANCE BOT
The Problem — Before Automation
Daily manual checking was slow, error-prone, and missed issues
Aura Jewels Pvt. Ltd. — Confidential
2 / 14
⏰
3–4 Hours Daily
Staff manually logged into 23 DVR/NVRs in iVMS-4200 every morning, clicking through 506 cameras one by one
🧠
Human Error
Easy to miss blurry cameras, cameras pointing wrong direction, or recording gaps during manual review
📋
No Records
No historical record of camera health. If a camera failed last week, nobody would know when it started
❌ BEFORE
✅ AFTER (with Bot)
• 23 DVR/NVRs checked manually
• 3–4 hours per day
• No written report
• Issues often missed
• All 23 DVRs checked automatically
• Under 5 minutes
• Excel report + database history
• Every camera logged with photo

## Slide 3
📹
CCTV
SURVEILLANCE BOT
System Architecture
How the bot connects to your camera network
Aura Jewels Pvt. Ltd. — Confidential
3 / 14
CAMERA NETWORK
📡
AGDVR 1–4
192.168.x.x
📡
AGNVR 1
192.168.x.x
📡
NEW DVR 1, 3
192.168.x.x
📡
DVR 6–9
192.168.x.x
📡
NVR-201–208
192.168.x.x
📡
Hi-tech DVR1–4
192.168.x.x
📡
Growth DVR
192.168.x.x
Hikvision
ISAPI
🤖 CCTV BOT
Python + Flask
🕐
1. Get DVR System Time
📋
2. Fetch Camera Names
📷
3. Capture Snapshot
🔍
4. Check Image Clarity
⏺
5. Verify Recording Status
💾
6. Save to Database
📊
7. Generate Excel Report
OUTPUTS
🌐
Web Dashboard
Live camera status
📊
Excel Report
Colour-coded per DVR
📸
Snapshots
Saved by date/DVR
🗄
SQLite DB
Full history stored
📧
Issues List
Flagged cameras

## Slide 4
📹
CCTV
SURVEILLANCE BOT
Connection Method — Hikvision ISAPI
The bot speaks directly to DVR/NVR hardware — no screen clicking
Aura Jewels Pvt. Ltd. — Confidential
4 / 14
💻
CCTV BOT
Python Script
HTTP Request
(Digest Auth)
JSON/XML Response
📡
DVR / NVR
Hikvision Device
ISAPI ENDPOINTS USED
GET
/ISAPI/System/time
— Get DVR clock — used as camera date/time (no OCR needed)
GET
/ISAPI/System/Video/inputs/channels
— Get all camera names and channel numbers
GET
/ISAPI/ContentMgmt/InputProxy/channels
— Get NVR camera names (newer devices)
GET
/ISAPI/Streaming/channels/{ch*100+1}/picture
— Capture live JPEG snapshot from each camera
POST
/ISAPI/ContentMgmt/search
— Search recordings — confirms camera is recording today
GET
/ISAPI/ContentMgmt/Storage/hdd/1
— Check HDD status — verifies storage is healthy

## Slide 5
📹
CCTV
SURVEILLANCE BOT
Camera Clarity Check — 6 Metrics
Every snapshot is analysed by computer vision algorithms
Aura Jewels Pvt. Ltd. — Confidential
5 / 14
1
📏
File Size
→ NO SNAPSHOT
> 3KB confirms snapshot received successfully
2
💡
Brightness
→ NO VIDEO / DARK
Mean < 12 = NO VIDEO
Mean < 38 = VERY DARK
Mean > 240 = OVEREXPOSED
3
🎨
Color Variance
→ LENS BLOCKED
Std deviation < 8 across pixels = lens blocked or covered
4
🔍
Center Sharpness
→ BLURRY
Laplacian variance on center 50% only — ignores soft edges of wide-angle lenses
5
🌙
Night Vision
→ NIGHT VISION
R/G/B channel difference < 6 = grayscale IR mode active
6
📅
Timestamp Visible
→ NO TIMESTAMP
White pixel density in top-left > 0.3% = timestamp OSD is on

## Slide 6
📹
CCTV
SURVEILLANCE BOT
Recording Verification — 3-Method Cascade
How the bot confirms cameras are actually recording
Aura Jewels Pvt. Ltd. — Confidential
6 / 14
↓ if fails
1
BEST METHOD
ContentMgmt Search API
POST to /ISAPI/ContentMgmt/search with today's date range.
Searches for actual recorded files in storage for this channel.
Returns numOfMatches — if > 0 recording confirmed.
↓ if fails
2
NVR METHOD
Track + HDD Status
GET /ISAPI/ContentMgmt/record/tracks/{trackID}
If track exists AND HDD status = "ok" → recording running.
Works for NVRs using scheduled recording (Enable=false is normal).
3
FALLBACK
Enable Flag Check
Check <Enable> tag in track config.
For old DVRs: true = recording ON, false = recording OFF.
For NVRs: always returns true (schedule mode).

## Slide 7
📹
CCTV
SURVEILLANCE BOT
Web Dashboard — 6 Sections
Live browser-based monitoring at http://localhost:5000
Aura Jewels Pvt. Ltd. — Confidential
7 / 14
📹 CCTV
🏠
Dashboard
Stats + DVR list
📡
DVR / NVR
All devices dropdown
🎥
All Cameras
506 cameras table
⚠️
Issues
Problems only
📅
Scan History
Past scans + Excel
📋
Activity Log
Live scan output
📊
7 Live Stat Cards
DVRs, Cameras, OK, Issues, No Video, Blurry, Errors — click any to jump to that filtered view
🔽
DVR Dropdown List
Click any DVR to expand — shows all cameras with clarity badge, recording dot, status icon
👁
Camera Preview + Viewer
Click View on any camera to see the live snapshot. Full-screen viewer with left/right arrow keys to browse
⚠️
Issues Page
Filter by No Video / Blurry / Dark / No Rec. Arrow navigation stays within current filter
📅
History + Excel Export
Every scan saved to SQLite. Each past scan has ↓ Excel button to download that specific day's report
🔐
Login Protected
Username: Admin Password: Auracctv#2024 Session persists across browser refresh

## Slide 8
📹
CCTV
SURVEILLANCE BOT
Excel Report — Auto-Generated
Colour-coded report saved to Desktop after every scan
Aura Jewels Pvt. Ltd. — Confidential
8 / 14
📊 CCTV_Report_DD-MM-YYYY.xlsx
Summary
All Cameras
DVR/NVR
Ch
Camera Name
Date
Time
Clarity
Rec
Status
AGDVR 1
1
AJ2_Filing 1
23-04
10:22
NIGHT
YES
OK
AGDVR 1
4
AJ2_Filing 2
23-04
10:22
CLEAR
YES
OK
DVR 9
2
POLISH RPR 2
23-04
11:46
BLURRY
YES
BLURRY
HiTech 1
7
Conference 01
23-04
11:47
DARK
YES
DARK
NVR-203
25
092.1st Pass
23-04
16:36
NO SNAP
YES
NO SNAP
AGNVR 1
1
Reception 1
23-04
10:44
CLEAR
YES
OK
COLOUR CODING
Green rows
Camera OK — clear image, recording confirmed
Red rows
Issue detected — blurry, dark, no snapshot, no recording
Orange rows
Warning — minor issues like date mismatch
REPORT FEATURES
✅ Auto-generated after every scan
✅ Saved to Desktop with today's date in filename
✅ Summary sheet + All Cameras sheet
✅ Auto-filter enabled — filter by DVR, status
✅ Frozen header row for easy scrolling
✅ Historical reports available from Scan History

## Slide 9
📹
CCTV
SURVEILLANCE BOT
Device Configuration — nvr_config.json
All 23 DVR/NVR credentials stored in one JSON file
Aura Jewels Pvt. Ltd. — Confidential
9 / 14
nvr_config.json
{
"dvr_nvr_list": [
{
"name": "AGDVR 1",
"ip_address": "192.168.2.237",
"port": 80,
"username": "admin",
"password": "p@ssword",
"enabled": true,
"skip_channels": [27,28,29,30,31,32]
},
{ "name": "NVR-201", ... }
// ... 21 more devices
]
}
23 DEVICES CONFIGURED
AGDVR 1–4
192.168.2.237–252 | Port: 80–83
AGNVR 1
192.168.0.254 | Port: 80
NEW DVR 1,3
192.168.2.243–250 | Port: 82–83
DVR 6–9
192.168.2.246–249 | Port: 86–90
NVR-201–208
192.168.100.201–208 | Port: 81–88
Hi-tech 1–4
192.168.3.245–247 | Port: 81–84
Growth DVR
192.168.70.201 | Port: 80
💡 skip_channels: channels with no physical camera are excluded from checks

## Slide 10
📹
CCTV
SURVEILLANCE BOT
Daily Scan Flow — Step by Step
What happens every time the bot runs
Aura Jewels Pvt. Ltd. — Confidential
10 / 14
1
▶
Start Scan
Click Run Scan button or schedule
via PM2 / Task Scheduler
2
📄
Load Config
Read 23 DVR/NVR credentials
from nvr_config.json
3
🔌
Connect DVR
HTTP Digest Auth to each device
Get system time via ISAPI
4
📋
Get Cameras
Fetch all channel names
Apply skip_channels filter
5
📷
Snapshot
GET /picture endpoint per channel
Save JPEG to snapshots folder
6
🔍
Clarity Check
6-metric OpenCV analysis
Flag issues: dark/blurry/blocked
7
⏺
Rec Check
3-method cascade verification
Confirm recording exists today
8
💾
Save & Report
SQLite DB + Excel file
Dashboard updated live

## Slide 11
📹
CCTV
SURVEILLANCE BOT
Data Storage & History
Every scan is permanently stored for future reference
Aura Jewels Pvt. Ltd. — Confidential
11 / 14
SQLite DATABASE STRUCTURE
🗄 scans
id
scan_date
scan_time
total_dvrs
total_cams
ok_count
issue_count
🗄 dvr_results
id
scan_id
dvr_name
ip_port
nvr_time
total_cams
ok_count
error
🗄 camera_results
id
scan_id
dvr_id
dvr_name
channel
cam_name
clarity
recording
status
snap_rel_path
SNAPSHOT FOLDER STRUCTURE
📁 snapshots/
📁 2026-04-24/
Today's scan
📁 AGDVR_1/
🖼 Ch01_AJ2_Filing_1.jpg
🖼 Ch02_AJ2_NM_1.jpg
📁 NVR-201/
🖼 Ch01_Reception_1.jpg
📁 2026-04-23/
Yesterday's scan
📁 2026-04-22/
Older scans...

## Slide 12
📹
CCTV
SURVEILLANCE BOT
Production Deployment — PM2
Always-running server like Node.js apps — never goes down
Aura Jewels Pvt. Ltd. — Confidential
12 / 14
01
Install Node.js
Required for PM2
$ Download from nodejs.org → Install LTS version
02
Install PM2
Process manager
$ npm install -g pm2
npm install -g pm2-windows-startup
03
Install Python requirements
One time only
$ pip install flask requests openpyxl urllib3 pillow opencv-python
04
Start with PM2
Starts the app
$ pm2 start ecosystem.config.js
05
Enable auto-start on reboot
Survives restarts
$ pm2 save
pm2-startup install
Useful: pm2 list | pm2 logs cctv-dashboard | pm2 restart cctv-dashboard | Access: http://localhost:5000

## Slide 13
📹
CCTV
SURVEILLANCE BOT
Results — Real Numbers
Actual scan statistics from Aura Jewels deployment
Aura Jewels Pvt. Ltd. — Confidential
13 / 14
📡
23
DVRs / NVRs
🎥
506
Cameras Checked
✅
478
All OK
⚠️
28
Issues Found
⏱
<5 min
Scan Duration
🌙
17
Night Vision Cams
🌫
5
Blurry Cameras
📵
4
DVR Errors
⏰ TIME SAVINGS
❌ BEFORE
3–4 Hours
manual daily check
→
✅ AFTER
< 5 Minutes
fully automated

## Slide 14
📹
CCTV
SURVEILLANCE BOT
Aura Jewels Pvt. Ltd.
🌐 http://localhost:5000
👤 Admin / 🔑 Auracctv#2024
BUILT WITH
Python
Flask
OpenCV
SQLite
PM2
What We Built
✅
506 cameras checked automatically
In under 5 minutes — was 3–4 hours manually
🔍
6-metric image quality check
Brightness, sharpness, blocked lens, night vision, timestamp
⏺
3-method recording verification
ContentMgmt search, HDD status, Enable flag cascade
🌐
Full web dashboard
Live status, history, preview, Excel export, login auth
💾
Permanent SQLite history
Every daily scan stored — trend analysis, export any day
🚀
PM2 production deployment
Always running, auto-restart, starts on Windows boot